## Slide 1: Connection Oriented and Connectionless Network

## Slide 2: connection-oriented Network
A connection-oriented service is a network service that was designed and developed after the telephone system
It Creates End –End Connection Between Sender and Receiver
In connection-oriented service, packets are transmitted to the receiver in the same order the sender has sent them
It uses a handshake method that creates a connection between the sender and Receiver before transmitting the data over the network.
Hence it is also known as a reliable network service.

## Slide 3: Cont…
receiver can respond to the sender in the form of Acknowledge .
After successfully exchanging or transmitting data, a sender can terminate the connection by sending a signal to the receiver.

## Slide 4
connection-oriented Network

## Slide 5
Delay in a connection-oriented network

## Slide 6: Connectionless Service
A connection is similar to a postal system, in which each letter takes along different route paths from the source to the destination address.
Connectionless service is used in the network system to transfer data from one end to another end without creating any connection.
So it does not require establishing a connection before sending the data from the sender to the receiver.
It is not a reliable network service because it does not guarantee the transfer of data packets to the receiver, and data packets can be received in any order to the receiver.
Therefore we can say that the data packet does not follow a defined path.
In connectionless service, the transmitted data packet is not received by the receiver due to network congestion, and the data may be lost.

## Slide 7
A connectionless packet-switched network

## Slide 8
Delay in a connectionless network
Notes: Waiting
time

## Slide 9: Difference Between Connection oriented and Connectionless
Sr.no | Features | Connection oriented | Connection less
1 | Definition | Performing handshaking | Not performing handshaking
2 | Connection | Prior connection is established | Prior connection is not established
3 | Speed | It is slow | It is fast
4 | Addressing unit | Circuit identifier is addressing unit | Network & host are identifier addressing unit
5 | Reliability | Reliable :acknowledgement | Not reliable
6 | Bandwidth use | As it used by circuit | Used by number and size of frame
7 | Impact of crashing | Complete circuit will crash | Only packet at node are lost
8 | Traffic processing | Signaling for path setup | Every packet route independently
9 | examples | Frame relay, ATM ,ISDN,PSTN | IP,ETHERNET
10 | Protocol Used | TCP | UDP